## Slide 1: Hall A DAQ meeting
April 6th 2015
Alexandre Camsonne

## Slide 2: Agenda
budget Compton ( Bob / Alex / Dave )
new BCM receiver / BCM calibration ( Luke ? )
BigBite DAQ status ( Alexandre )
silo file transfer errors ( Bob / Ole ? )
SoLID review outcome DAQ recommendations ( JP / Alexandre )
upcoming experiment preparation (GMp/DVCS, Ar ee'p, APEX ) ( Alexandre )
SBS Fastbus status and plan (Dasuni ?)
SBS trigger distribution scheme ( Alexandre )
SBS cerenkov trigger and readout using VETROC ( Alexandre - same as what was presented at SBS meeting )

## Slide 3: Budget Compton
for integrating mode DAQ
1 ..... Gate Generator, 2 VME scalers, .... 19
Spare V1495, spare V538A
for counting mode DAQ;
assume we use existing FADC
2 ..... VXS Crate, cpu, TI ................ 22
3 ..... Prototype VETROC .................. 5
(~ 1 year later need 5 production
boards for a total of 40K$)
To buy after the single plane recently installed
is demonstrated to work
4 ..... Thick silicon for E-det .......... 38
3 planes for 26K$
7 for 35K$
10 for 38K$ (preferred)

## Slide 4: BCM new receiver down

## Slide 5: BCM new receiver up

## Slide 6: BCM new receiver RF source
https://logbooks.jlab.org/entry/3322081

## Slide 7: BCM new receiver RF source
https://logbooks.jlab.org/entry/3322081

## Slide 8: Standard 1MHz BCM
Offset from 1 MHz box about -15 mV
Added linear fan
x3 saturates at about 15 uA
x10 saturates above 5 uA
Need to check overlap of different gains
Need low current data for calibration linearity check
3 options
  Keep this way if x10,x3 and x1 cover whole range
  Revert back no fan ( should be ok 15 mV = 0.2 uA )
  Get Musson to open the 1 MHz box and adjust offset

## Slide 9: BigBite DAQ status
3 CPUs
1 crate trigger with new TI with 1877S
1 crate triggering from back with 1877S
1 crate bad 5V PS fixed
Few bad slots will replace bin when tests done
Need program V1495
New computer would be handy

## Slide 10: SoLID review DAQ

## Slide 11: SoLID review DAQ

## Slide 12: SILO transfer errors
A few files did not get transferred regularly
Second script to check and resubmit : works fine
Ole might have found the issue

## Slide 13: Upcoming experiment
Low energy runnning
  Coincidence trigger for Ar (ee’p) ?
  1 DAQ for both HRS
  Need Aerogel ?
  Need efficiency trigger for proton

## Slide 14: APEX plan
Mostly same as Gmp
  Coincidence trigger
  FADC for SciFi detector : install VME64X crate in Right HRS ( 11 FADC for HCAL , need 8 )
  Need implement TDC sparsification
  Include FPP ?
  Optional : deploy new TI in parallel to standard TI to have event blocking option

## Slide 15: SBS Trigger scheme
Presented to SBS review

## Slide 16: SBS Trigger scheme
New TI scheme

## Slide 17: SBS Trigger scheme
Use on TS for pipeline DAQ and Fastbus
Use trigger partitioning ( trigger part of DAQ depending on the trigger ) feature of new TS
Need new TI
Advantage :
  TS takes care of flipping ( could try to get rid of V1495 and do in TS )
  One data stream

## Slide 18: SBS Cerenkov Trigger

## Slide 19: SBS meeting VETROC application for Cerenkov triggering
Alexandre Camsonne
March 18th 2015

## Slide 20: VETROC board
Developped for Compton and SoLID MRPC
64 input + 8 input and 8 output
Extension with mezannine to 128 channels (compatible with V1495 mezzanines )
Optical link
VXS link for triggering purpose
Will try to develop high resolution TDC ( possibly 25 ps resolution )
Estimate price around 2.5 K$ for 64 channels and about 4 K$ for 128 channels

## Slide 21: vXS fPGA-based Time to Digital Converter (vfTDC)
Trigger Interface
Trg/Clk/Reset/Busy
4x fiber Tx/Rx
VXS P0:
Trg/Clk/Reset/Busy
32 LVTTL in
32 differential in
Generic
8 differential In
8 ECL out
32 LVTTL in (with mezz. for differential IN)
32 differential in
28 LVTTL on row A
4 + 4 LVTTL on row D
28 LVTTL on row C
VME64x:
Register,
Data Readout
FPGA, XC7A200T-2FF1156C
18Mbit RAM
preliminary

## Slide 22: Pipelined electronics
250 MHz sampling
4x 3 GBps Optical fiber link
Can process hits every 4 ns or 8 ns
Readout VME320 : 200 MB/s ( 5 times faster than Fastbus )

## Slide 23: (1) Simple FPGA logic
Fast, potentially no crate
OR of all AND of a 3 channels
Cerenkov trigger
In about 200 ns max
Or of all VETROC output

## Slide 24: (2) Pipeline logic VME64X
128
X
8
=
1024
Optical links
4x3 GBps
Optical links
4x3 GBps
SSP
Trigger latency :
250 ns ( serialisation / deserialisation )
15 ns data
50 ns Processing
Trigger in about 350 ns for 1024 channels

## Slide 25: (3) Pipeline logic VXS
CTP
VXS lanes 5 GBps
VXS lanes 5 GBps
Up to 16 VETROC per VXS crates : 2048 channels
Trigger latency :
250 ns ( serialisation / deserialisation )
15 ns data ( 128 bits per board )
50 ns Processing
Trigger in about 350 ns

## Slide 26: (4) Hybrid pipeline logic VXS
Up to 16*8=128 VETROC = 16384 channels
VETROC
VME64X
crates
16 x SSP and 1 GTP in VXS crate
Channels = 2048 * crates
Latency
Serialization VXS VETROC-SSP 250 ns
Serialization SSP 250 ns
Serialization VXS SSP-GTP 250 ns
Data transfer = 2048 / 8 GBps = 256 ns per crate
Processing 500 ns
Trigger latency about 2 us for 2 crates

## Slide 27: (5) Full fledge pipeline logic VXS
Channels = 2048 * crates
Latency
Serialization VXS VETROC-CTP 250 ns
Serialization CTP – SSP 250 ns
Serialization SSP-GTP 250 ns
Data transfer = 2048 / 8 GBps = 256 ns per crate
Processing 500 ns
Trigger latency about 2.3 us for 2 crates
VETROC
VXS
Crates
16 VETROC
Per crate
=
2048
16 x SSP and 1 GTP
Up to 128 x 2048 channels
=
262,144

## Slide 28: Readout
High resolution TDC available at readout stage ( could be made available at trigger level but need redesign ) : preliminary resolution 20 ps on 128 channels
VME320 : 140 MB/s sustained
Can fully take advantage of event blocking

## Slide 29: GRINCH
550 PMT
Option (2)
5 x VETROC = 5x4K$ =20 K$
1 VME64X crate = 8 K$
1 SSP = 5 K$
1 TI = 4 K$
1 CPU = 4 K$
Total about 41 K$

## Slide 30: RICH
2400 channels
Option (4)
  1 VME64X crates = 8 K$ = 8 K$
  1 VXS crate = 15 K$
  2 CPU = 2 x 4 K$ =16 K$
  1 GTP = 6 K$
  2 TI = 2 x 3 K$ = 6 K$
  3 SSP = 3 x 5 K$ = 15 K$
  1 TD = 4 K$
  19 VETROC = 19 x 4 K$ = 76 K$
Total = 146 K$

## Slide 31: RICH
2400 channels
Option (5)
  3 VXS crate = 3x 15 K$ = 45 K$
  2 CTP = 2 x 5 K$ = 10 K$
  3 CPU = 2 x 4 K$ =12 K$
  1 GTP = 6 K$
  3 TI = 2 x 3 K$ = 6 K$
  1 SSP = 5 K$
  19 VETROC = 19 x 4 K$ = 76 K$
Total = 160 K$

## Slide 32: RICH triggers
Have all PMTs every 4 ns
  Clustering
  Ring ?
If redesign of firmware logic to have high resolution at L1
  Could have time over threshold and have amplitude at L1
  Cut on single PMT amplitude
  Threshold on digital sum all PMTs
  Threshold on digital sum on ring or clusters

## Slide 33: Conclusion
VETROC can form prompt trigger and do readout
Pipeline logic can be used for more complicated triggers ( more latency around 300 ns ) might be still fast enough for L1A within a crate, can be used for L2 with HCAL
Cost ranges from
High resolution readout developed 25 ps resolution
Might be able to have high resolution at trigger level with investment