## Slide 1: SuperBig Bite DAQ
Use of standard Fastbus with pipeline Flash ADC for Hadron Calorimeter and APV25 GEM tracker readout
Fastbus
  1800 calorimeter channels
  16 crates
  6 Power Supply
  New CODA 3 electronics improve deadtime by 30%
  19 controller, 28 bin, 12 PS,176 TDC,6200 ADC channels tested
Trigger
  Analog sum ECal
  Coincidence ECAL HCAL
  10 KHz coincidence rate
GEM trackers
  6 Front trackers INFN
  8 Rear chamber
  APV25 readout
  Custom VME readout INFN
  Readout ported to Linux VME controller
  Start implementation in JLAB DAQ environment
  Analog trigger for electromagnetic calorimeter and Big Bite
  Digita trigger for HCAL
FADC for HCAL
  242 channels
  16 FADC
  Digital summing for triggering
  2 VXS crate, 4 FADC received for R&D