## Slide 1: SBS DAQ
SBS collaboration Meeting
Alexandre Camsonne
July 13th 2017

## Slide 2: Outline
GMn ERR
GEp plan
GEM data reduction
HCAL progress
Fastbus
Network upgrade
DAQ disks
SILO capability
Tape cost
TDIS TPC
Manpower
Simulation work
Conclusion

## Slide 3: Expected trigger rates GMn
Q^2 | n+p QE xsec | L(per atom) | QE rate | Beam time | Total
GeV^2 | fb | 10^38/cm^2/s design | Hz | Hours | Hz
3.5 | 6700 | 0.35 | 235 | 12 | 2100
4.5 | 1015 | 0.7 | 70 | 12 | 1400
5.7 | 97.9 | 1.4 | 13.5 | 18 | 140
8.1 | 47.4 | 1.4 | 6.6 | 18 | 390
10.2 | 31.6 | 0.7 | 1.5 | 24 | 210
12 | 5.04 | 1.4 | 0.7 | 36 | 200
13.5 | 6.25 | 1.4 | 0.87 | 96 | 100
Maximum trigger rate 2.1 KHz, assume factor 2 safety margin for 4.2 KHz for low Q2
less than 500 Hz at high Q2
Single electron trigger is a good option
( possibility to add Cerenkov in the trigger if needed )
Preferably single electron trigger to avoid biased in neutron detector

## Slide 4: GEM occupancy and data rates
occupancies from Q2 = 13.5 GeV2, with luminosity 2.8 10^38 A-1 cm-2 s-1 (44uA on 10cm LD2 target) and rates from low Q2 point : 1.3 KHz
 | Rate per (KHz/cm2) | Rate per plane (MHz) | hits in 325 ns | Occupancy (%) | strip hits | x2 XY (strips) | x6 samples | Evt size (bytes) | Rate MB/s
1 | 89.6 | 537.6 | 174.72 | 27% | 612 | 1223 | 7338 | 29357 | 123.30
2 | 101.6 | 609.6 | 198.12 | 31% | 693 | 1387 | 8321 | 33284 | 139.79
3 | 101.4 | 608.4 | 197.73 | 30% | 692 | 1384 | 8305 | 33219 | 139.52
4 | 98.1 | 588.6 | 191.295 | 29% | 670 | 1339 | 8034 | 32138 | 134.98
5 | 89.3 | 535.8 | 174.135 | 27% | 609 | 1219 | 7314 | 29255 | 122.87
 |  |  |  |  |  |  |  | Total | 660.46
Worse case scenario using High Q2 occupancies with low Q2 rates
Deconvolution on SSP : expect factor of 3 reduction about 220 MB/s

## Slide 5: Data rates GEp5
Detector | Rate | Channels | Occupancy | Data size Bytes | Data rate MB/s 5 KHz 3 samples | Geometrical factor | Data size geo Reduc MB/s | Double for 6 samples MB/s
Front Tracker | 400.00 | 49000.00 | 1 | 589149 | 2946 | 3.00 | 919 | 
Second Tracker | 130.00 | 61440.00 | 1 | 738720 | 3694 | 5.00 | 660 | 
Third Tracker | 64.00 | 61440.00 | 1 | 738720 | 3694 | 5.00 | 660 | 
Total |  | 171880.00 |  | 2066589 | 10332 |  | 2459 | 4918
Need further reduction by using deconvolution and maybe clustering on SSP

## Slide 6: Front Tracker layout
2048 channel
1 MPD
2048 channel
1 MPD

## Slide 7: Trackers layout
1 MPD
2048
1 MPD
2048
Front tracker
Region of
Interest from
BigCal position
Back tracker
Region of
Interest from
HCal position
Middle tracker
Interpolated from both front
and
back information

## Slide 8: Trackers layout
Worst
case
configuration

## Slide 9: FPP Tracker layout
512
2560
2048

## Slide 10: Geometrical MPD suppression
Different methods
  Use on user input Fast clear MPD
    pro : MPD stay in synch
    con : need more MPD firmware work
  only issue trigger for modules of interest and have SSP keep track of number of events to be read
    pro : no change to MPD
    con : MPDs out of synch and rely on SSP for synchronization, more firmware work
  do on SSP or VTP
    pro : no hardware change
    con : resource intensive, synchronization issues, more work for Ben !

## Slide 11: MPD fastclear
ECAL
HCAL
L2A
FC1
FCn

## Slide 12: MPD Fastclear timing
0
L1
200 ns
L2
Start reading APV
1000 ns
FC
2000 ns
1
Samp
L
E
4525 ns
6th
S
a
m
p
l
e
21150 ns
Send data to
SSP
25000 ns

## Slide 13: SSP readout performances
Nb samples | Blocklevel | Rate (kHz) | Effective rates (kHz) | Effective rates 8 APV (kHz) | Data rate | 
1 | 1 | 23 | 23 | 8.6 | 26 | 
3 | 1 | 15 | 15 | 5.6 | 50 | 
3 | 2 | 15 | 15 | 5.6 | 100 | 
3 | 4 | 7 | 28 | 10.5 | 85 | 
3 | 4 | 10 | 40 | 15 | 100 | No transfer
1 backplane, 3 APVs, no zero suppression
Disk speed : 98.2 MB/s
Network : 117 MB/s
Backplane VME : 100 MB/s
Can saturate backplane
Expected rate around 15 KHz per MPD

## Slide 14: Timeline GEM
Implement first pass SSP data reduction this summer: common noise suppresion running average, 6 samples discard first and 6th sample if highest amplitude
Second pass if required January 2018 with higher priority from Electronics group
( CLAS12 run in October )

## Slide 15: Fastbus readout
Time : 1877S
Amplitude 1881M
Fastbus max transfer speed : 40 MB/s can use either Intel or Old vxworks VME CPU
ECal : 4 sets of 3 crates, will be able to test performance about 50 MB/s at 100 % occupancy
Cdet : 9 Fastbus crates about 11 MB/s at 10 % occupancy

## Slide 16: Fastbus
Good progress from Bob
Tools to check synchronization available
still development to handle event blocking in decoding

## Slide 17: HCAL readout
288 channels
2 VXS crates , 18 FADCs
1.5 MHz singles
16 block clusters
FADC 250 MHz 12 bit = 2 bytes
10 samples : 320 bytes , 57.6 MB/s at 100 % occupancy
VETROC or F1 : high resolution TDC, need NINO
VTP need to developped
2 VETROC for ECAL sums input and MPD fast clear

## Slide 18: VTP
New Hall B CTP
Larger FPGA than GTP
2x10 Gig optical links
Plan development of VXS readout for FADC and possibly SSP
7 K$
Have 2 for HCAL

## Slide 19: HCAL trigger status
VTP installed
Firmware loaded, need testing
No CODA ROC planned for CODA 2.6 only for CODA3 so no VTP readout
  Need to negotiate with DAQ group for CODA 2.6 for readout
  Or need to upgrade all Fastbus CPU to Intel for VTP readout ( 10 GigE )
  or readout VTP with a CPU or PC at 10 gigE

## Slide 20: Network upgrade
Replace hall A router with an Arista switch, reuse existing hall A router as the switch for the racks. This provides dense 10Gig aggregation, with 40Gig expandability. Estimate $30K, 3 month lead time.
Single Mode Fiber Installation in the hall ( required for any speeds>1Gbit/sec), rough estimate $30K, 6 month lead time.
  Counting House to left arm, 24 strand
  Counting House to right arm, 24 strand
  Counting House to Labyrinth, 24 strand
  Counting House to Hall Floor Rack Area, 24 strand
40Gig uplinks to CEBAF center ($20K upgrade to item 2).
Bottomline : 10 Gig capability 30 K$ + temporary fiber 10 gigE

## Slide 21: Counting house DAQ disks
Raid array on adaq3
several disks
1GB/s seems doable
Might need to upgrade to hold 72 hours of data : 259 TB
( Hall D about 28 K$ per raid array )

## Slide 22: SILO capabilities
Mix of LTO 5 and 6
  14 drives LTO 5 and 6 = 2 GB/s
  up to 16 drives
  each LTO7 drive is 300 MB/s about 10 K$ each
  Max : 16 * 300 = 4.8 GB/s
  to handle 1 GB/s : 4 drives about 30 K$
  increase to 4 GB/s ( 1GB + dup + read ) about 120 K$
  need to write and read at same time
  LTO8 available in 4 to 5 years
  Need to let IT know our real needs might need more drives

## Slide 23: Tape cost
 |  | Days | Weeks | Data rate | Seconds | Total data TB | Double | LTO5 in k$ | LTO6 in k$ | LTO7 in k$ | LTO8 in k$
E12-12-09-019 | GMN | 25 | 3.57 | 500 | 2160000 | 1080 | 2160 | 108 | 65 | 27 | 13
E12-09-016 | GEN | 50 | 7.14 | 500 | 4320000 | 2160 | 4320 | 216 | 130 | 54 | 25
E12-07-109 | GEP/GMP | 45 | 6.43 | 1000 | 3888000 | 3888 | 7776 | 389 | 233 | 97 | 46
E12-09-018 | SIDIS | 64 | 9.14 | 1000 | 5529600 | 5529.6 | 11059.2 | 553 | 332 | 138 | 65
 | Total | 184 | 26.29 |  | 15897600 | 12657.6 | 25315.2 | 1,265.76 | 759.46 | 316.44 | 148.33

## Slide 24: TDIS
BNL TPC readout
https://eic.jlab.org/wiki/index.php/Trigger/Streaming_Readout
streaming TPC readout

## Slide 25
Streaming Readout concept
25
The streaming data are recorded all the time, and broken up in chunks above threshold
Only chunks correlated with triggered events are then kept
✖
✖
✖
✖
This results in a greatly reduced data stream
The real-time processing demands are very high

## Slide 26
The streaming TPC readout
DAM Data Aggregation Module
EBDC Event Buffering and Data Compressor
Buffer Box
To RCF/
HPSS
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Data Concentration
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DAM
EBDC
DAM
EBDC
DAM
EBDC
DAM
EBDC
DAM
EBDC
DAM
EBDC
10+ Gigabit
Crossbar
Switch
TPC
Same components as shown before

## Slide 27
Front-End – ALICE SAMPA Chip
ASIC developed for ALICE for the TPC
More functionality than we would need while streaming
10Ms/s @ 10Bit -> 100Mbit/s internally, 32channels
This oversubscribes its external links
Above-threshold waveform delivery – send chunks of the waveform around samples “sticking out” above a threshold + bookkeeping
Estimate 5 samples/channel/hit and 3 channels -> 15 samples/”hit”
8 Sampa chips on one Front-end card – 256 channels
~400 FEE cards

## Slide 28
Data path overview
Buffer box
+
ATLAS Felix PCIe card
Up to 48 FEE->Card
(48 fibers)
About 10 PCs (EBDC) with
one FELIX card each

## Slide 29: Man power
Fastbus/ECAL
  M. Jones, B. Michaels, J. Gu, B. Moffit
HCAL
  B. Raydo, A. Camsonne
GEM readout
  E. Cisbani, B. Moffit, A. Camsonne, P. Musico, B. Raydo, S. Riordan, D. Di
BigBite : E. McLelan

## Slide 30: Simulation work
Test data reduction algorithm on simulated data for GEM
Occupancies different detectors GMn, Gep for different kinematics start to look at SIDIS, TDIS

## Slide 31: Conclusion
Need evaluate data rates after reduction for all experiments especially GEp5 aiming at 500 MB/s (no major upgrafe )
If more than 1 GB/s need network/SILO/disks upgrade need to discuss with IT
Ongoing development on SSP : first iteration end of summer
HCAL trigger in testing
Good progress Fastbus
Look ahead future experiments SIDIS, TDIS