## Slide 1: SBS DAQ overview
Alexandre Camsonne
February 26th 2019
SBS Collaboration meeting

## Slide 2: Outline
Neutron Form Factors experiments
GeP
SIDIS
TDIS
Data rates
Upgrade plan
Conclusion

## Slide 3: Experimental setup GMn
BigBite
  Shower
  Preshower
  Scintillator
  GRINCH
  ( check Eric’s talk )
  GEM
Neutron detector
  CDET
  HCAL
LHRS
Detector | Channels | NINO | Readout | ADC | TDC
Shower | 7x27 = 189 27 sums |  | Fastbus | X | 
Preshower | 2x27 =54 2 sums |  | Fastbus | X | 
Scintillator | 200 x 2 | X | VME | X | X
GRINCH | 550 | X | VME |  | X
GEM | 5 planes |  | VME |  | 
Detector | Channels | NINO | Readout | ADC | TDC
HCAL | 288 |  | VME | X | X
CDET | 2352 | X | Fastbus |  | X

## Slide 4: SBS GMn DAQ Overview
Calorimeter
  ECAL : Fastbus
  HCAL :FADC , F1 or VETROC TDC
SBS GEM
  APV25 INFN MPD
BigBite
  Scintillator
  Shower preshower
  Fastbus
Coordinate detector
  Fastbus

## Slide 5: SBS Gen RP DAQ Overview
Additionnal detectors
2 Hodoscope arrays 24+24 scint bars from (Old) BB Hadron stack 2 PMTs/bar 96 HV, signal channels)
10 'Rear' GEM planes 6 in-line with SBS detector stack 2 in front of 'left' hodoscope array (proton pol.) 2 in front of 'right' hodoscope array (proton pol.)
Electronics
6+2 F250 FADC Draw from 'NPS/LAD' FY19 plans (*)
1 C1190 TDC In hand (1+spare: Glasgow + Hall C spares)
6+2 CAMAC Discrim. 4 in hand; 4 to locate
1 VXS crate In hand (1+spare: Glasgow + Hall C spares**)

## Slide 6: GRINCH readout
6 VETROC ordered for Compton
6x128 = 768 channels
Backplane board ordered for 192 channels
4 boards for Compton
Existing initial prototypes : 2 x 192
Using spare Compton crate 1 VXS crate spare desired ( 15 K$)

## Slide 7: Glasgow Hodoscope readout
VME based
  V1190 TDC
  V792 QDC
  VME64X crate
Existing drivers already
CODA setup beginning of 2019

## Slide 8: Inventory GMn/GEn
TS : VXS crate, TS, TD, 1 Intel CPU
HCal
  288 channels : 18 FADCs, 2 VXS crates ( JLAB + UVA ), 2 VTP, 2SD, 2 CPU, 2 TI, 5 F1 TDC
BigBite
  243 shower channels : 4 Fastbus ADC, 1 SFI (from ECAL), 1 TI ( from ECAL)
  90 hodoscopes bar = 180 channels : NINO + 3 V1190 ( Glasgow ) + 2 V792 (Glasgow) + 1 VME64X crate
  550 GRINCH : 3 or 5 VETROC + VXS crate + 1 GTP + 1 CPU + 1 TI
  4 INFN GEMs 1 UVA GEM : 1 VXS crate (UVA)+ 2 VME 64 X crate ( JLAB + UVA ) + 20 MPDs + 4 SSP (Hall A+C) + 1 SD (SBS) + 3 CPUs + 3 TI
Cdet
  2520 channels
    NINO + 9 Fastbus crates +9 SFI +9 INTEL CPU + 27 TDC 1877S ( 3 per crate )
LHRS
  768 VDC channel on 3 Fastbus crates, 3 SFI, 3 new TI (ECAL) , 3 intel CPU ( from ECAL )
  2 S0, 32 S2m on F1 ,10 Cerenkov ,68 channels Pion Rejector on Fastbus

## Slide 9: GMn tasks
BigBite ( see Eric’s talk )
GEM readout
HCal
CDet

## Slide 10: GMn tasks
BigBite ( see Eric’s talk )
GEM readout
  SSP readout with Danning suppression working for 4 MPD
  New firmware with new event structure and L2 clear installed end of 2018
  SSP readout for 32 MPDs Summer 2019

## Slide 11: GMn tasks
Cdet
  only one crate right now
  all hardware needed
  start spring or summer 2019 full Fastbus system
HCal
  HCAL readout working for one crate though reduce set of channels ( APEX using 10 FADCs)
  need to test 2 crates readout ( need VXS crate )

## Slide 12: GMn
Switch to CODA3 ?
  need to use all new intel CPUs
  VTP readout options : 10 gigE capability

## Slide 13: GEp
Coincidence trigger and
ECAL readout :
  analog trigger
  Fastbus fast readout
HCal trigger :
  1 crate trigger working
  2 crate trigger and ECAL coincidence and GEM
GEM readout : need test full scale system

## Slide 14: GEM occupancy and data rates GMn
occupancies from Q2 = 13.5 GeV2, with luminosity 2.8 10^38 A-1 cm-2 s-1 (44uA on 10cm LD2 target) and rates from low Q2 point : 1.3 KHz
 | Rate per (KHz/cm2) | Rate per plane (MHz) | hits in 325 ns | Occupancy (%) | strip hits | x2 XY (strips) | x6 samples | Evt size (bytes) | Rate MB/s
1 | 86 | 516 | 167.7 | 26% | 586.95 | 1173.9 | 7043.4 | 28178 | 118.35
2 | 94 | 564 | 183.3 | 28% | 641.55 | 1283.1 | 7698.6 | 30794 | 129.34
3 | 93 | 558 | 181.35 | 28% | 634.725 | 1269.45 | 7616.7 | 30467 | 127.96
4 | 92 | 552 | 179.4 | 28% | 627.9 | 1255.8 | 7534.8 | 30139 | 126.58
5 | 54 | 324 | 105.3 | 16% | 368.55 | 737.1 | 4422.6 | 17690 | 74.30
 |  |  |  |  |  |  |  | Total | 577
Worse case scenario using High Q2 occupancies with low Q2 rates
Deconvolution on SSP : expect factor of 3 reduction about 190 MB/s

## Slide 15: Gep GEM data rates
 | Rate per cm2 | Rate per plane | hits in 325 ns | occupancy | strip hits | XY | 6 samples | bytes | Rate MB/s
1 | 540 | 3240 | 1053 | 100% | 3240 | 6480 | 38880 | 155524 | 777.62
2 | 610 | 3660 | 1189.5 | 100% | 3660 | 7320 | 43920 | 175680 | 878.40
3 | 670 | 4020 | 1306.5 | 100% | 4020 | 8040 | 48240 | 192960 | 964.80
4 | 720 | 4320 | 1404 | 100% | 4320 | 8640 | 51840 | 207360 | 1036.80
5 | 740 | 4440 | 1443 | 100% | 4440 | 8880 | 53280 | 213120 | 1065.60
 |  |  |  |  |  |  |  | Total | 4723.22
Column1 | Column2 | Column3 | Column4 | Column5 | Column6 | Column7 | Column8 | Column9 | Column10
 | Rate per cm2 | Rate per plane | hits in 325 ns | occupancy | strip hits | XY | 6 samples | bytes | Rate MB/s
1 | 280 | 1680 | 546 | 84% | 1911 | 3822 | 22932 | 91732 | 458.66
2 | 270 | 1620 | 526.5 | 81% | 1842.75 | 3685.5 | 22113 | 88452 | 442.26
3 | 260 | 1560 | 507 | 78% | 1774.5 | 3549 | 21294 | 85176 | 425.88
4 | 260 | 1560 | 507 | 78% | 1774.5 | 3549 | 21294 | 85176 | 425.88
5 | 230 | 1380 | 448.5 | 69% | 1569.75 | 3139.5 | 18837 | 75348 | 376.74
 |  |  |  |  |  |  |  | Total | 2129.42
Column1 | Column2 | Column3 | Column4 | Column5 | Column6 | Column7 | Column8 | Column9 | Column10
 | Rate per cm2 | Rate per plane | hits in 325 ns | occupancy | strip hits | XY | 6 samples | bytes | Rate MB/s
1 | 140 | 840 | 273 | 42% | 955.5 | 1911 | 11466 | 45868 | 229.34
2 | 135 | 810 | 263.25 | 41% | 921.375 | 1842.75 | 11056.5 | 44226 | 221.13
3 | 135 | 810 | 263.25 | 41% | 921.375 | 1842.75 | 11056.5 | 44226 | 221.13
4 | 130 | 780 | 253.5 | 39% | 887.25 | 1774.5 | 10647 | 42588 | 212.94
5 | 135 | 810 | 263.25 | 41% | 921.375 | 1842.75 | 11056.5 | 44226 | 221.13
 |  |  | Total |  | 7958.32 | MB/s |  | Total | 1105.67
 |  |  | Geometrical Factor |  | 2652.772031 | MB/s |  |  | 
 |  |  | SSP reduction |  | 884.2573438 | MB/s |  |  | 
 |  |  | Drop to 3 samples |  | 442.25 | Mb/s |  |  | 

## Slide 16: Data rate GEp
Ecal : 40 MB/s
Hcal : 63 MB/s
Cdet : 11 MB/s
Total 1 GB/s

## Slide 17: SIDIS

## Slide 18: Occupancies / data rates
Assume 5 KHz trigger rate

## Slide 19: Data rates SIDIS
Column1 | Column2 | Column3 | hit | Column4 | strip | XY | 6 samples | bytes | Column5 | Rate | Column6 | Rate MB/s | 
1 | 50 | 300000000 | 97.5 |  | 390 | 780 | 4680 | 18720 |  | 93600000 |  | 93.6 | 
2 | 50 | 300000000 | 97.5 |  | 390 | 780 | 4680 | 18720 |  | 93600000 |  | 93.6 | 
3 | 50 | 300000000 | 97.5 |  | 390 | 780 | 4680 | 18720 |  | 93600000 |  | 93.6 | 
4 | 50 | 300000000 | 97.5 |  | 390 | 780 | 4680 | 18720 |  | 93600000 |  | 93.6 | 
5 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
 |  |  |  |  |  |  |  |  |  |  |  | 499.2 | 
Column1 | Column2 | Column3 | hit | Column4 | strip | XY | 6 samples | bytes | Column5 | Rate | Column6 | Rate MB/s | 
1 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
2 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
3 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
4 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
5 | 50 | 400000000 | 130 |  | 520 | 1040 | 6240 | 24960 |  | 124800000 |  | 124.8 | 
 |  |  |  |  |  |  |  |  |  |  |  | 624 | 
 |  |  |  |  |  |  |  |  |  | Total |  | 1123.2 | MB/s
 |  |  |  |  |  |  |  |  |  | SSP reduction |  | 374.4 | MB/s
About 400 MB/s at 5 KHz trigger rate

## Slide 20: TDIS data rates
From Paul’s talk
  up to 0.6 GB/s per chamber = 6 GB/s total with 160 ns integration time
  80 ns integration time and smaller pads can help
  would help to reduce data with tracking
    can that be done in FPGA of SSP / VTP
    L3 farm ? ( coming back in fashion with streaming readout so maybe work out at deal with IT and management )

## Slide 21: Network upgrade
Replace hall A router with an Arista switch, reuse existing hall A router as the switch for the racks. This provides dense 10Gig aggregation, with 40Gig expandability. Estimate $30K, 3 month lead time.
Single Mode Fiber Installation in the hall ( required for any speeds>1Gbit/sec), rough estimate $30K, 6 month lead time.
  Counting House to left arm, 24 strand
  Counting House to right arm, 24 strand
  Counting House to Labyrinth, 24 strand
  Counting House to Hall Floor Rack Area, 24 strand
40Gig uplinks to CEBAF center ($20K upgrade to item 2).
Bottomline : 10 Gig capability 30 K$ + temporary fiber 10 gigE for GMn
Full upgrade : for Gep, SIDIS, TDIS additionnal 50 K$

## Slide 22: Infrastucture status (500 MB/s) 2020
Item | Status
LHRS DAQ | 1 intel CPU 4 Vxworks CPU
Computer disks | 2 raid arrays 2000 MB/s
Network | Gigabit ethernet in Hall (100 MB/s) 10 GigE router 10 Gig adapter on adaq1 and adaq2 ( 1000 MB/s) 1 fibers 10 Gig Ethernet to Silo ( 1000 MB/s )
Silo | 8 drives LTO5 8 drives LTO6 4 LTO7 ( 300 MB/s) 4 LTO8 ( 360 MB/s) -> 5 GB/s
Current infrastructure should satisfy GMn and Gen close from limit for only
high rate point

## Slide 23: Infrastucture should (1GB/s) 2021/2022
Item | Status | Cost
LHRS | 1 intel CPU 4 intel CPU | 15 K$
Computer disks | 2 raid arrays 2GB/s 8 SSD ( 8x 2GB/s ) | 20 K$
Network | 1 Gigabit ethernet in Hall 40 GigE router 40 Gig adapter on adaq1 and adaq2 ( 1000 MB/s) 2 fibers 10 Gig Ethernet to Silo ( 2000 MB/s ) | 30 K$ 5 K$
Silo | 8 drives LTO5 8 drives LTO6 4 LTO7 ( 300 MB/s) 4 LTO8 ( 360 MB/s) 4 LTO8 ( 360 MB/s) -> 6.2 GB/s | 40 K$ (IT)
Moderate upgrade 70 K$: can easily handle GMn and GEn, can test CODA3,
should be ok for Gep unless bad background surprise
Easy upgrade to 40 gigE, can take full advantage of VTP readout

## Slide 24: Infrastucture like ( 5 GB/s capability)
Item | Status | Cost
LHRS | 1 intel CPU 4 intel CPU | 15 K$
Computer disks | 2 raid arrays 2GB/s 8 SSD ( 8x 2GB/s ) 1 PB disk array | 20 K$ 300 K$
Network | 10 Gigabit ethernet in Hall 40 GigE router 40 Gig adapter on adaq1 and adaq2 ( 5000 MB/s) 2 fibers 40 Gig Ethernet to Silo ( 8000 MB/s ) | 30 K$ 30 K$ 5 K$ 20 K$
Silo | 8 drives LTO5 8 drives LTO6 4 LTO7 ( 300 MB/s) 4 LTO8 ( 360 MB/s) 14 LTO8 -> 11.2 GB/s | 40 K$ (IT) 140 K$ (IT)
Safe for Gep, TDIS and future program, can use fast VTP readout
120 K$ upgrade + 300 K$ disk + 140 K$ silo
( could delay silo and large disk for better cost and upgrade every year)

## Slide 25: Conclusion
GMn
  BigBite
  HCal DAQ OK
  Finalize Cdet DAQ
  Switch to CODA3
  Ready by fall 2019
GeP ( busy year 2019 2020 )
  finalize coincidence trigger
  test full scale DAQ
  ECAL
SIDIS
  similar setup as GMn and Gen + RICH
  GEM rate about 400 MB/s
TDIS : need major upgrade and / or efficient way to reduce data from 6 GB/s to about 1 GB/s