## Slide 1: Summary streaming readout workshop
Alexandre Camsonne

## Slide 2: Streaming readout workshop
Jan 29-30, 2018
https://eic.jlab.org/wiki/index.php/Streaming_Readout_II

## Slide 3: Streaming readout definition
Triggerless DAQ
Each detector just stream events it considers of interest independently : no event building
Global timestamp to put events together

## Slide 4: Slide from Graham

## Slide 5: LHCb
Talk by Mike Williams
https://eic.jlab.org/wiki/images/9/96/Mike_Williams.pdf

## Slide 8: New JLAB developements
Chris Cuevas talk
https://eic.jlab.org/wiki/index.php/File:Chris_Cuevas.pdf

## Slide 9: CLAS12 RICH readout

## Slide 10: Streaming without crates
Readout/Control of ASIC <-->Network
C. Dickover
B. Raydo
DAQ Group
JLAB FPGA Readout/Control Board
192 Channel Interface
Algorithms
  1ns TDC
  Scaler
Fixed Latency up to 8us
Optical Ethernet – Use Commercial 1Gbe
  Finisar Transceiver capable of 10Gbps
  Artix could run @3.125Gpbs
Mates to MAROC3 or other ASIC
+5VDC @1A
Xilinx Artix7
Commercial 1Gbe LC Fiber Network Switch
Test with many ports
  Will need SYNC to each card
  How will Network manage SYNC?
  Need Firmware Change
Test Data Rates
Test Ability to synchronize data from each FPGA card.
Scale of test can increase quickly
  i.e. 10 FPGA boards ~2K channels
  Streaming Data
MAROC3
Or
Use Internally Generated Data
DATA PROCESSOR

## Slide 11: FADC
FADC can inherently stream data
Just need bandwidth to ship all the data :
  16 channels x 250 MHz x 16 bits (12 bits ADC ) = 8 GB/s per board
Fast serial readout : optical, PCI express, VXS or Ethernet ( 40 Gbit )

## Slide 12: New 500 MHz FADC

## Slide 14: Standalone FADC

## Slide 15: Streaming DAQ through VXS trigger processor
C
Built In Self Test
Hits Generate TDC Data
14 Boards
1344 Wires
SBC
‘64x
VXS
VME
A
B
Simulated Wire Chamber ‘Hits’
  DATA
  24bit words; 17 bits time; 7 bits Channel
  This is a large range but 1ns resolution!
Each DCRB board has 10Gb/s [1.25GB/s] link to VTP [ 4 lanes/@3.125bps * (0.8 Encoding) ]
  Test limitations of VTP serial collection of 14 DCRB ‘Payload’ boards
  Synchronous data is not an issue because all boards are in the same crate
  VTP must consume 17.5GB/s [14 Boards]
40Gbe from VTP “CODA Read_Out_Controller”
Test VTP data processing capabilities and throughput
  96 channels from each DCRB will probably be an issue for DDR memory on VTP
  What problems will we face to interface with 40Gbe network switch?
  What happens when we have more than one crate?
Bypassing VME64x Example
A
B
C
SSP
SSP
SSP
DCRB
VTP
1GHz Dual Core ARM
Processor [Xilinx Zynq] (Linux OS)

## Slide 16: More examples of VXS readout/control of ASIC
C. Dickover
B. Raydo
CEA Saclay**
INFN*
RICH 25,000 pixels
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
SBS GEM
+40K pads
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
DREAM
FPGA
MPD*
APV25
MicroMegas
+20K strips
Forward Tracker
+3300 uMegas Strips
FPGA
FEC**
VME64x Readout Bandwidth [~200MBs]
OK Because
Detector occupancy
Is low (~1%)
Imagine using
VTP in each of
these examples
to bypass VME

## Slide 17: FADC calorimeter readout
Use Existing PbWO4 Crystals as prototype detector
    Neutral Particle Spectrometer (preferred, as want to make 25-100 crystal prototype anyways)
    GlueX Forward Calorimeter Upgrade
    Heavy Photon Search Calorimeter
Hall A DVCS (PbF2) Calorimeter recorded full waveform 128 samples
Now: Test readout & resulting resolution to constrain full waveform with 4 samples
Develop parallel readout of flash ADCs through serial link = 16 x 125 Mb/s
Test readout & resulting resolution to constrain full waveform with 4 samples
Can also test to transfer only clusters from flash ADCs
NPS Pulse Fairly Fast, ~ 50 ns total

## Slide 18: Future Experiments: JLab NPS & SoLID
Neutral Particle Spectrometer:
1000+ channel electromagnetic PbWO4 calorimeter in high background area
SoLID:
Large Acceptance Detector operable at High (1037-39) Luminosity
The detector has two configurations. In the PVDIS configuration electrons are scattered of a fixed target at high luminosity.
The detector is split into 30 sectors with a single track event topology.
Current proposal 30 DAQ systems to be run in parallel at rates of 1 GByte/s each with custom electronics to deal with tracks that cross sector boundaries.
Complex system relying on coordination of the semi-independent DAQs
Sweeping magnet before EM calorimeter to reduce background rates and achieve up to 1039 luminosity
Readout with PMT and HV divider linear to within 2% for up to 2 MHz/crystal.
Plan to use flash ADCs to read full wave form
vertex
tracking
PID
EMCAL
HCAL
muon
e
γ
K/π/p
μ
ν
jets
PTmiss
absorber
Prediction: all calorimeter readout will start using full wave forms

## Slide 19: Streaming readout on hit level
Detector response (t)
streaming readout
use RF as t0
select time windows
build events
Data monitoring Anomaly detection
Detector modelling
Learn detector responses
Events
EIC detector
RF
synchronized
machine learning
machine learning

## Slide 20: Streaming readout on event level
Physics analysis
Storage
Data monitoring
Anomaly detection
Physics analysis
Operation
Event
Event
Event
Operation
Stream of events
Type of operations
Align
Calibrate
Filter
Tracking
PID
Filter for data quality
Selection of events according to type (trigger)
Alignment and calibration obtained from set of events

## Slide 21: Conclusion
Progress in technologies is making streaming DAQ more and more accessible
Straightforward for simple detectors and already existing
Still main issue is data reduction for large granularity and high background detectors such as GEM trackers
Needs more computing and or storage power but gives more flexibility