## Slide 1: ECAL FADC DAQ

## Slide 2: Gep5 calorimeter geometry
1792 channels of lead glass

## Slide 3: HPS scheme

## Slide 4: VTP trigger
Same as HCAL with 2x2 clusters

## Slide 5: FADC crates ECAL SBS
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
SSP

## Slide 6: Neighbors only
One crate = 16 x16 channels

## Slide 7: FADC crates ECAL SBS
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
CPU
VTP
SD
TI
FADC
FADC
Transfer neighbors and do clustering on each VTP : 64 channels instead of 256

## Slide 8: Integral + time
FADC can record up to 4 pulses in time window
Data about 10 times smaller if reading 25 samples

## Slide 9: Waveform
Hall A DVCS recorded full waveform 128 samples

## Slide 10: Waveform
NPS pulse fairly fast, need to check with final base and cable length

## Slide 11: VTP readout
VTP readout
  VME backplane limited to 100 MB/s
  Development of parallel readout of FADC through serial link = 16x 125 MB/s
  good option for cluster readout ( read all FADC and only transfer clusters )

## Slide 12: Cost estimates total
 | Number needed | Unit price K$ |  |  | 
1792 channels | 112 |  |  |  | 
Cost estimation |  |  |  |  | 
FADC 250 | 4500 | 112 | 504000 |  | 
TD | 3000 | 1 | 3000 |  | 
SSP | 4000 | 1 | 4000 |  | 
Transceiver | 400 | 7 | 2800 |  | 
VTP | 7000 | 8 | 56000 |  | 
TID | 3000 | 8 | 24000 |  | 
SD | 2500 | 8 | 20000 |  | 
VXS crate | 15000 | 8 | 120000 |  | 
VME CPU | 3400 | 8 | 27200 | No FADC | 
 |  | Total | 761000 | 257000 | 

## Slide 13: Conclusion
For 1792 calorimeter channels
7 VXS crates
VTP readout to be able to read cluster only
About 257 K$ assuming all 112 FADC can be borrowed from electronics pool