## Slide 1: HRS TOF setup
Alexandre Camsonne

## Slide 2: Single arm and coincidence
TOF between S0 and S2
  information on particle momentum ( usually much worse than momentum ), can be used for PID
TOF between Left S2m and Right S2m
  best timing resolution
  long path length
  also used for PID
  useful for ee’p, Kaon, APEX

## Slide 3: Corrections
Offsets : cable, TDC offset fixed, usually use overlap or reference scintillator to calibrate
Time propagation in scintillator
Timewalk effect
Pathlength correction
RF timing

## Slide 4: Example transversity experiment
http://hallaweb.jlab.org/data_reduc/AnaWork2009/BigBite-Coincidence-Time-Calibration-Jin.pdf

## Slide 5: Coincidence TOF
BigBite was 270 ps timing resolution : should be able to do better with two HRS

## Slide 6: Readout
Old way : Fastbus 1875 50 ps
New TDCs
  F1 : 60 ps 32 channels
  V1290 : 25 ps 32 channels
  VETROC : 20 ps 128 channels

## Slide 7: RF signal
499 MHz signal from accelerator
Allow to know the time with reference to the bunch
250 MHz now if 4 halls are running

## Slide 8: Plan
Deploy 2F1 TDC in both HRS
  copy of S2m
  test V1290 and VETROC in Test Lab
  add V1290 and VETROC in one arm to compare performance and split F1 signal
Send RF signal to TDC
  found signal
  most likely prescaled by 8 to be easier to handle