## Slide 1: Hypernuclear Physics in Hall A
E07-012 Status
John J. LeRose
December 16, 2009

## Slide 2
Proposal E07-012 to study the angular dependence of p(e,e’K+)Λ and 16O(e,e’K+)16Λ N at Low Q2
http://www.jlab.org/exp_prog/proposals/07/PR-07-012.pdf
Approved PAC January, 2007
Scheduled to run April 19-May 14, 2012
The last 6 GeV era experiment in Hall A

## Slide 3
The kinematics of the proposed experiment. | 
Incident Electron Energy | 3.65 GeV
Virtual photon energy | 2.2 GeV
Q2 | 0.0789 (GeV/c)2
Electron scattering angle , θe | 6°
Kaon scattering angle , θKe | 8.5° & 11°
Kaon momentum, ¦pK¦ | ~1.96 GeV/c
Electron Momentum, ¦pe¦ | ~1.45 GeV/c

## Slide 4: E07-012 expected Data

## Slide 5
Electroproduction on 16O - angular distribution
Simultaneously measuring the electroproduction cross section on oxygen and hydrogen at a few kaon scattering angles will shed new light on problems of hypernuclear physics AND discriminate between groups of elementary models

## Slide 6: Good News / Bad News
 Qweak will run
 Qweak wants all the cryogens it can get
  Must build a room temperature septum pair à la PREX
Runs in parallel with Qweak

## Slide 7: Re Room Temperature Septa
Two not quite identical RT septa will work
Same iron but different coils
  RTlight: for 6° electron side (B=0.737 T)
    Reduced coil allows close proximity to the beam line
  RTstd: for 8.5° & 11° Kaons (B=1.215 & 1.51 T)
    Beefier coil, but doesn’t have to get as close to the beam line
Benefits from the PREX experience
  But there’s work to do.

## Slide 8: PREX Magnet Status and Capabilities
John J. LeRose
with much help from Paul Brindza

## Slide 9: PREX Magnet assembled in the Physics storage Building

## Slide 10: General Charateristics
Design is a twin dipole
RT septum fields can be anti-parallel or parallel
RT anti parallel has a quadrupole on axis
RT parallel has net dipole on axis
Iron beam filter works for PREX fields (0.5 T) but is saturated for hi field(1.2 T) running
“PREX” uses 2 of 3 coils and iron fillers for better field uniformity
“Hi field” uses all 3 coils and reaches 1.2 T at expense of uniformity

## Slide 11: RT septum geometry
Iron gap 24 cm high x 30.25 cm wide x 75 cm long
“PREX” coil have 80.64 cm^2
“PREX” J is 600 Amp/cm^2
“PREX” can run w/o a booster LCW water pump
“Hi field” coil is 161.76 cm^2
“Hi field” J is 850 Amps/cm^2
“Hi Field” requires a LCW water booster pump

## Slide 12: Magnetic performance
“PREX” NI = 96,768
“PREX” By(23.7, 0,0) = 0.4997 T
“PREX” ∫By(23.7,0,z)dz= 0.485 T.M
  G(1,0,0)=8.2 g/cm ∫G.dZ = 1739 (g/cm)cm
“Hi Field” NI = 274,992
“Hi Field” By(23.7,0,0)= 1.21 T
“Hi Field” ∫By(23.7,0,z)= 1.21 T.M
  G(1,0,0)=658 g/cm, ∫G.dz = 50,624 (g/cm)cm

## Slide 13
5° PREX configuration | right | left
phi min | -0.026 | -0.018
phi max | 0.018 | 0.026
theta ± | 0.043 | 
P0 max (GeV/c) | 1.11 | GeV/c
PREX ∫Bdl | 0.485 | T∙m
Hi Field ∫Bd | 1.21 | T∙m
Hi Field P0 max (GeV/c) | 2.77 | GeV/c

## Slide 14
a
b
l1
l2
l3
γ
target to pivot @ 5° | 1054 | mm
Bend angle @ 5° (α) | 7.5 | deg
HRS angle @ 5° (γ) | 12.5 | deg
target to pivot @ 9° | 506 | mm
Bend angle @ 9° (α) | 6.5 | deg
HRS angle @ 9° (γ) | 15.5 | deg

## Slide 15
Chart: ~ΔΩ
| -250 | -125 | 0 | 125 | 250
~ΔΩ1 | 4.1378 | 4.1739 | 4.1251 | 3.9038 | 3.1705
~ΔΩ2 | 0.96882 | 1.0033 | 1 | 0.94321 | 0.77951
Left axis, ΔΩ1, assumes rectangular acceptance i.e. neglects acceptance loss from rounded corners, a slight overestimate.
Right axis, ΔΩ2, just calculates the relative number of trajectories for each case.
“PREX” at 5°. Just move the target upstream and downstream.
Chart: Central Scattering Angles (°)
| -250 | -125 | 0 | 125 | 250
Central Angles | 4.8712 | 5.0894 | 5.3173 | 5.6361 | 5.9769

## Slide 16: Summary
“PREX” magnet adds lots of small angle capability
  5°< central angle < 12°
  Either polarity in either arm
  High current with thick targets
BUT:
  Momentum range is limited
    1.11 GeV/c or 2.77 GeV/c at 5°
  Must have the same angle on both sides

## Slide 17: Backup Slides

## Slide 18
Chart: Z0 beam = -250 mm
“PREX” at 5°. Just move the target upstream and downstream.
Chart: Z0 beam = 0
Chart: Z0 beam = 250 mm