## Slide 1: E12-07-108: (GMp) Precision Measurement of the Proton Elastic Cross Section at High Q2
Vincent Sulkosky
Massachusetts Institute of Technology
for the E12-07-108 Collaboration
Spokespeople: J. Arrington, E. Christy, S. Gilad, B. Moffit,
V. Sulkosky, B. Wojtsekhowski
Hall A Collaboration Meeting
June 13th, 2013

## Slide 2: Goals for GMp
Accurately measure e-p elastic cross section in
kinematics similar to other JLab form factor
measurements
Improve accuracy of the cross section by as much as a
factor of 4 (< 2%) over previous measurements
Key input to all form factors and many of other
experiments, where elastic scattering is a background
Provide measurement of power scaling for GMp
in the range Q2 = 7-14 GeV2
Approved for 24 PAC days

## Slide 3: Control of Systematics
DAQ and Trigger:
  EDTM pulser for dead time measurements
  Achieved 10 kHz with 20% dead time
Tracking efficiency:
  Use front chambers of FPP with VDCs
Target density
  Use precise optics to provide software cuts on vertex
  Use race-track cell targets with vertical flow to
  minimize fluctuations
Solid angle: a benefit of improved optics
Scattering angle: precise determination of
target location using strong arm wire target

## Slide 4: Modifications to Instrumentation
Strong arm wire target:
  Design completed
  Cost: $3k to $5k, saved $8k by using old radiator mechanism
HRS detector stacks:
  Design completed
  Add one chamber of FPP to both stacks
  Attach S0 to FPP chamber
  Shorten extension box for LHRS gas Cherenkov by 10 cm
  Cost: $20k (mostly from labor, trying to reduce this cost)
Target scattering chamber
  Design completed, though there maybe modifications
  Allows to run DVCS (LHRS) and GMp (RHRS) concurrently
  Cost: ~ $50k

## Slide 5: HRS Optics and Angle: Wire Target
Wire target, reproducibility of 100 microns sufficient Design completed, waiting on order of parts
Wires:
0.5” apart along the
beamline
1/16” (~1.6 mm)
apart transverse to
beam

## Slide 6: HRS Detector Stacks
Standard detectors with one plane of FPP
VDCs
Pion rejector
Gas Cherenkov
Fpp
S0

## Slide 7
New Narrow DVCS Support Stand

## Slide 8
Restrictions from scattering chamber design:
  LHRS: 12.5o to < 48o (> 18o with calorimeter)
  RHRS: -33.7o to < -78o (> 45o with calorimeter)
  DVCS calorimeter: < -20o
Angle Restrictions

## Slide 9
Target Configuration
Solid targets/Endcaps measured with x-ray attenuation
LH2: 15 cm Racetrack:
Vertical flow design
Dedicated studies of density
Luminosity monitors in
datastream
Not compatible with DVCS
Solid Al Foils (Dummy):
Endcap subtraction
Carbon Optics Targets:
1-2 cm spacing along zvertex for extended target acceptance

## Slide 10
Target Density/Boiling
Results from x>2, Z. Ye (UVA)
Simulation by Silviu Covrig

## Slide 11: Expected Precision

## Slide 12: Systematic Uncertainties
Source | Point-to-point | Normalization
Incident energy | <0.3 | 
Scattering Angle | 0.1-0.3 | 
Incident Beam Angle | 0.1-0.2 | 
Radiative Corrections* | 0.3 | 0.4
Beam Charge | 0.3 | 0.4
Target Thickness/Density Fluctuations | 0.2 | 0.5
Spectrometer Acceptance | 0.4-0.8 | 0.6-1.0
Endcap Subtraction | 0.1 | 0.1
Detector efficiencies/dead time | 0.3 | 0.4
Sum in quadrature | 0.8-1.1 | 1.0-1.3
Uncertainties give in Δ/ (%)

## Slide 13: Tasks & Responsibilities
Tasks | Commitments
Scattering chamber design | JLAB – A. Gavalya
Strong arm wire target design | Hall A – J. Miller
Online analysis software | JLAB – A. Camsonne, O. Hansen
LH2 Target | JLAB – D. Meekins, J.-P. Chen
Beam line | Hall A – D. Higinbotham, B. Michaels, E. Christy
Refurbish Gas Č counter ( measure mirrors, test/replace PMTs) | MIT – K. Allada, V. Sulkosky, L. Ou, Y. Wang
VDC electronics, crates | YerPhi – A. Shahinyan
FPP | YerPhi – A. Shahinyan et al.
NIM trigger electronics | Hall A – B. Wojtsekhowski
Analysis for absolute cross-sections | HU – E. Christy
Scattering and solid angle determination | ANL – J. Arrington

## Slide 14: Graduate Students
Longwu Ou (MIT)
Yang Wang (W&M)
Mohamed Nuh Hashir Rashad (ODU);
DVCS graduate student
Potential student from HU and perhaps another
from MIT (Barak Schmookler)

## Slide 15: Commitments in Manpower
FPP work: Albert Shahinyan, Galust Sargsyan and Karen (YerPHI)
HRS detectors:
  Milan Dukic (NCCU technician) for three weeks
  Hamza Atac (Temple) for two weeks
  NSU student for one month
  Longwu Ou (MIT); (GMp student)
  Kai Pan (UVa student) for two weeks
  Puneet Khetarpal (FIU postdoc) for two weeks
  John LeRose (JLab) part time
  Mohamed Nuh Hashir Rashad (ODU); DVCS graduate student
  Yang Wang (WM); graduate student (GMp student)

## Slide 16: Summary
Additional manpower is needed and welcome,
especially for testing of both spectrometers’
detector packages
GMp will provide a baseline for the 21st century level of accuracy in form factor measurements by precisely measuring the cross section at Q2 up to 14 GeV2.
It is the only measurement of the cross section; key input to all form factors and many of other experiments.
Some progress is being made with many of the improvements aiding other experiments that plan on using the HRS’s during 12 GeV.
GMp requires high precision at full 11 GeV beam energy!
Collaborators are welcome to participate; much work is still required before 2014.

## Slide 17: Backup

## Slide 18: Systematic Uncertainties
Source | Δ/ (%) | Parameters
Incident energy | <0.3 | 3×10-4
Scattering Angle | 0.1-0.3 | 
Incident Beam Angle | 0.1-0.2 | 
Radiative Corrections* | 0.3 | 
Beam Charge | 0.3 | 1×10-3
Target Density Fluctuations | 0.2 | 
Spectrometer Acceptance | 0.4-0.8 | 0.1 mrad
Endcap Subtraction | 0.1 | 
Detector efficiencies/dead time | 0.3 | 
Sum in quadrature | 0.8-1.1 | 
Point to point uncertainties

## Slide 19: Systematic Uncertainties

## Slide 20: FPP (front chambers)
Already 1 FTE year has been spent on FPP
Problems: gas consumption > 50 l/h HV trips often
due to gas, many dead wires/some electronics.
Done: repair of dead electronics; built parallel gas
distribution.
Still to do: HV distribution in one PC; gas distribution
should be as wide as a straw block; HV test
wires.
Recent: First chamber main work is completed;
second in progress and expect completion in
1 month; hardware electronics not yet started.

## Slide 21
VDC Improvements
Upgrade electronics to use
1877S, which allows sparsification
Replace aging A/D cards and reuse BigBite cards
Provide very good stability against
oscillations and rate capability
of 8 MHz (in full chamber)
LHRS and RHRS completed
and tested
Software still needed for Fpp
chamber and for cosmics
checks

## Slide 22
Gas Cherenkov Improvements
Reflectivity measurements of HRS GCC mirrors in progress
  Both HRS mirrors completed
  Two spare mirrors recoated and checked
Reflectivity is within a few percent of published results
In progress of checking relative response of PMTs and will replace those as needed; ~ 70 to test
Cosmic mirror calibration

## Slide 23: Introduction

## Slide 24
Kinematics
PAC Approved 24 days

## Slide 25
DVCS-GMp Cooperation: Dual Running
GMp and DVCS install together (except DVCS calorimeter)
GMp runs independently:
  Restrictions on HRS angles from vacuum chamber and DVCS stand
  Restrictions on HRS movement from DVCS cables and stand, HRS movement will require manual assistance
One week shutdown to install DVCS calorimeter
DVCS runs ~ 3 PAC months:
  GMp takes parasitic data with right HRs at large angles