## Slide 1: Apex Target
Marco Oriunno, April 23, 2014

## Slide 2
Design and fabrication by:
Marco Oriunno, Dieter Walz, Jim McDonald, Clive Field, Douglas Higginbotham, and many others…

## Slide 3: Requirements
Beam parameters assumed
40 µA
Vertical width 400 µm
Horizontal width 400 µm
Vertical dither 5 mm
Horizontal dither 1.5 mm
.

## Slide 4: General Layout
Beam direction
First Row (from the top) Carbon foils 100um, calibration of the spectrometer with wide angle pion. The first foil is probably BeO.
Second Row: Wires H/V for low current beam position and angle scanner.
Third Row: Tungsten Foil 15um (more stable that Tantalum). More foils downstream increase the Rate.

## Slide 5: Production target:
10 layers of 15 µm thick tungsten ribbons (4.3% rad length)
2.5 mm wide in X
Separated by 5.5 cm along beam
- Tracks from A´ decays produced in a ribbon, and going into the spectrometers, will not be intercepted by the next ribbon

## Slide 7: Target issues:
At 40 µA, the target will become hot!
The tungsten will expand
- The frames that hold the tungsten have enough spring to maintain the ribbons under tension, even when hot.
The hot tungsten may be much weaker than at room temperature
- The temperature range and tension are selected to stay away from breaking point.
- 250 g tension (Verify the tension is still 250 g)
Cooling in the beam region is mostly by black-body radiation. Conduction becomes more important at lower temperatures closer to the supports.
Numerous calculations of thermal effects and a simulation allowing for temperature dependence of thermal properties:--

## Slide 8: Temperature Transient (black body radiation only)
Peak temp
1300 K
Steady State after 20 sec.

## Slide 9: Temperature Distribution
Across the beam width
Temp. fairly uniform horizontally across ribbon

## Slide 10: Thermal Expansion
Elongation
130 µm

## Slide 11: Alignment relative to target
Beam at < 5 µA for alignment work
A set of tungsten wires spaced along the length of the target
4 horizontal wires in 5 mm vertical steps, at -25, -10, 10, 25 cm along the beam
3 vertical wires in 0.25 mm horiz steps, at -20, 0, 20 cm along the beam
100 µm diameter tungsten
Still gets hot! But not as bad as the production target ribbons.
- Still, use similar tensioning technique as for the ribbons
- 150 g tension

## Slide 12: Tungsten wire Calibration Target - Heating
Peak temp
900 K

## Slide 13: Calibration Target - carbon foils
Produce copious pion signal
8 foils spaced along the length of the target
(-30, -22.5, -15, -7.5, 7.5, 15, 22.5, 30 cm)
Target frames are mounted on an aluminum plate
Plate is cooled by N2 flow through heat sinks on reverse side
Optical targets for use during installation are inserted in the back of the plate, (ruby balls)
The wire positions have been surveyed relative to the optical alignment targets.
BeO scintillator for beam diagnostics

## Slide 14: Work that should be done on the target
-Visually inspect it
-Check that the target ribbons and wires are under adequate tension
-Check that the structure is clean enough for vacuum
-I believe that one or two of the target ribbons were made of
tantalum, the intention being to hedge our bets and
see if either metal survived better during special
test runs (not carried out).
The tantalum was found to be mechanically liable to
crack during flexing.
->Decide whether to replace the tantalum with tungsten.