## Slide 1: APEX Trigger and DAQ
Sergey Abrahamyan
Yerevan Physics Institute
APEX collaboration

## Slide 2: Overview
Requirements
Trigger improvements
DAQ improvements
Summary

## Slide 3: HRS Detectors
Central Ray
2 PMTs
LHRS Calorimeter
S2m
Gas Cherenkov
Total 4 layers
368 wires each
VDC
S0
16 Paddles
10 PMTs
2 segmented layers of lead glass blocks
RHRS Calorimeter
Notes: Scintillators used for timing and triggers
Left HRS
34 blocks in each layer
15x15x30cm dimensions
Right HRS
48 blocks in preshower
10x10x35cm dimensions
75 blocks in shower
15x32.5x15cm dimensions
Used for PID
Right arm GC used as part of trigger to achieve pion rejection on trigger level

## Slide 4: Detector channels
Detector | Detector Channels | DAQ channels
Gas Cherenkov | 10 | 10 time 10 amplitude
Scintillators | 17 | 17 time 17 amplitude
Calorimeter | 128 – RHRS 68 – LHRS | 128 amplitude 68 amplitude
VDC | 1472 | 1472 time
RHRS
172 amplitude channels – 3 ADC modules
1516 time channels – 16 TDC modules
LHRS
112 amplitude channels – 2 ADC modules
1516 time channels – 16 TDC modules

## Slide 5: Trigger rate
Setting | A | B | C | D
Energy (GeV) | 2.2 | 4.4 | 1.1 | 3.3
e- (kHz) | 4500 | 700 | 6000 | 2900
π- (kHz) | 100 | 2200 | 36 | 1000
e+ (kHz) | 31 | 3.6 | 24 | 23
π+ (kHz) | 100 | 2200 | 36 | 1000
Trigger
Reduce coincidence timing
Suppress pions
Possible Improvements
DAQ
Using of sparsification

## Slide 6: Trigger Logic
Electron Arm Trigger (T1)
  Electron S2m
Positron Arm Trigger (T3)
  Positron S2m
Coincidence Trigger (T4)
  Electron S2m + Positron S2m
“Golden” Coincidence Trigger (T6)
  Electron S2m + Positron S2m + Positron Gas Cherenkov

## Slide 7: Timing Alignment in Hardware
Run at high rates, small timing gate is important
Must align timing of the trigger detectors
  S0 counter as a reference
  Inserted 1-5 ns delay cables
Electron S2m
Positron S2m
Positron GC
Chart: After adjustment
Left S2m (#1634) | 57.3 | 59.65 | 57.6 | 59.1 | 59.7 | 58.15 | 60.05 | 58.9 | 59.75 | 60 | 60.1 | 59.15 | 60.5 | 59.7 | 59 | 59.6
Right S2m (#1640) | 51.05 | 49.95 | 51 | 50.7 | 50.35 | 50.9 | 50.15 | 50.8 | 51.3 | 50.45 | 52.05 | 51.5 | 50 | 49.65 | 49.8 | 49.5
Right GC (#1729) | 39.95 | 39.6 | 40.45 | 40.7 | 40.8 | 39 | 40.5 | 39.1 | 41 | 40.25
σ Spread
0.9 ns 3.2 ns
0.7 ns 2.6 ns
0.7 ns 2 ns
Spread

## Slide 8: Coincidence Timing
20ns
20ns
10ns
Electron S2m pulse
Positron S2m pulse
Positron GC pulse
20 ns coincidence time easily achievable
Ideally 10ns could be used
40 ns timing gate
10 ns coincidence peak
Trigger Timing Diagram
Trigger moment
Time difference between Electron S2m and trigger
Time (ns)
Notes: T6 timing defined by GC
Reason for increase in accidentals (higher rates): more targets and larger solid angle
Improvement: factor 5 from timing
factor 10 from correcting multiple target hits

## Slide 9: Gas Cherenkov in Positron Arm (high rate)
30 μA on Pb Target
Positron arm rate – 765 kHz
(close to maximum expected rate)
e + sample
p + + m+ sample
+ + m+ sample from LG
e + sample from LG
Electron detection eff. 0.992
Pion rejection eff. 0.970
Meson background rejected by a factor of 30
This analysis didn’t use timing
and coordinate information
Notes: Smaller rejection factor due to a higher rate of e+ (e+ occur same time pi+)

## Slide 10: Lead Glass Particle ID in Positron Arm (high rate)
Electron detection eff. 0.977
Pion rejection eff. 0.985
Meson background rejected by a factor of 60
This analysis didn’t use coordinate information
p + + m+ sample
e + sample
+ + m+ sample from GC
e + sample from GC
30 μA on Pb Target
Positron arm rate – 765 kHz
EPS – Energy deposition in 1st layer
ESH – Energy deposition in 2nd layer
p – Particle momentum

## Slide 11: Trigger rate
Setting | A | B | C | D
Energy (GeV) | 2.2 | 4.4 | 1.1 | 3.3
e- (kHz) | 4500 | 700 | 6000 | 2900
π- (kHz) | 100 | 2200 | 36 | 1000
e+ (kHz) | 31 | 3.6 | 24 | 23
π+ (kHz) | 100 | 2200 | 36 | 1000
T6 rate (kHz) 20ns window π+ rejection = 30 | 3.2 | 4.5 | 3.0 | 4.4
For 4 kHz DAQ dead time is 10%
APEX can run without any improvement to DAQ!

## Slide 12: 3 Crate configuration
RHRS
172 amplitude channels – 3 ADC modules
1516 time channels – 16 TDC modules
Crate 1: 5 TDC + 1 ADC
Crate 2: 5 TDC + 1 ADC
Crate 3: 6 TDC + 1 ADC
LHRS
112 amplitude channels – 2 ADC modules
1516 time channels – 16 TDC modules
    Crate 1: 5 TDC + 1 ADC
    Crate 2: 5 TDC + 1 ADC
    Crate 3: 6 TDC
By reducing number of channels which go to each crate we reduce the amount of data to be recorded and improve dead time.

## Slide 13: Sparsification
Common Stop
Start from background
Start from signal
full- scale window
0-32 µs (8ns step)
Sparsification
0-8µs
(0.5ns step)
Gate
Typical TDC spectrum without sparsification. Only 300ns window out of 1.5µs full scale window has useful data
Enabling of sparsification allows to significantly reduce event size. All TDC modules have been tested to work in sparsification mode.

## Slide 14: TDC test setup

## Slide 15: TDC test procedure
Sparsification CRL #1
Full scale time window = 400 ns
Sparsification threshold = 0 ns
Sparsification CRL #2
Full scale time window = 400 ns
Sparsification threshold = 300 ns
Sparsification CRL #3
Full scale time window = 496 ns
Sparsification threshold = 424 ns
0 ns
325 ns
400 ns
325 ns
300 ns
Common stop
Sparse. Thresh.
Sparse. Thresh.
0 ns
325 ns
400 ns
Common stop
Common stop

## Slide 16: Event Blocking
Readout
Triggers
Readout
Overhead
Readout
Overhead
Readout
Overhead
Overhead
Triggers
Readout
Readout
Readout
Readout
Overhead
For one channel readout.
4 events no EB – 280 µs
4 events with EB – 220 µs
20µs 50µs 20µs 50µs 20µs 50µs 20µs 50µs
20µs 50µs 50µs 50µs 50µs
Readout time is 50 µs + 2 µs per 16 channel.
64 channels – 58 µs
128 channels – 66 µs

## Slide 17: Event Blocking test results
Event Blocking | Number of channels | Number of modules | Life time (%)
1 | 1 | 1 | 71
4 | 1 | 1 | 90
1 | 64 | 3 | 65
4 | 64 | 3 | 80
20 kHz rate
New TI version 3
Linux CPU

## Slide 18: Summary
20 ns coincidence window and factor 30 online pion rejection in Right HRS should be enough to keep DAQ rate under 4.5 kHz
10 ns window and factor 50 online rejection is not impossible
DAQ can operate with 10% dead time at 4 kHz
DAQ dead time can be improved by easy steps of implementing sparsification and using 3 crate configuration (both hardware and software are ready to use)
Further improvement could be done by using event blocking