Instruction for Target Operation during PVDIS test runs, June 15-17
- Should use only two positions during the test:
  - “Empty” for empty;
  - “Optics” for the single carbon foil target;
- Always mask the target motion (call MCC) before moving the target!
- Monitor RTD temperatures (should be near room temperature ~25C, and must be less than 300 C at all time) from:
  - “Target cell temperature strip” chart or
  - EPICS “RTD Readback” GUI
- Monitor cooling jet flow (middle room camera), should be more than 35
- DO NOT move to “polarized 3He” or “pick-up coil” position, they may hit the cooling jet!