## Slide 1
Spectrometer optics studies and target development for the 208Pb(e,e’p) experiment in Hall A at Jefferson Lab ,
GUIDO M. URCIUOLI, INFN, Roma, Italy,
JUAN CARLOS CORNEJO, Cal. State Univ., Los Angeles,
JOAQUIN LOPEZ HERRAIZ, Univ. Complutense de Madrid,
JEFFERSON LAB HALL A COLLABORATION

## Slide 2
CEBAF and Hall A at JLab
e- source
Hall A

## Slide 3
JLAB Hall A Experimental setup
The two High Resolution Spectrometer (HRS) in Hall A @ JLab
Beam energy: 4.0, 3.7 GeV
E/E : 2.5 10-5
Beam current: 10 - 100 A
Targets : 12C, 208Pb, 209Bi
Run Time : approx 6 weeks
HRS – QQDQ main characteristics:
Momentum range: 0.3, 4.0 GeV/c
p/p (FWHM): 10-4
Momentum accept.: ± 5 %
Solid angle: 5 – 6 msr
Minimum Angle : 12.5°

## Slide 4: HRS Main Design Performaces
Maximum momentum (GeV/c) 4
Angular range (degree) 12.5-165°
Transverse focusing (y/y0)* -0.4
Momentum acceptance (%) 9.9
Momentum dispersion (cm/%) 12.4
Momentum resolution ** 1*10-4
Radial Linear Magnification (D/M) 5
Angular horizontal acceptance (mr) ±30
Angular vertical acceptance (mr) ±65
Angular horizontal resolution (mr) ** 0.5
Angular vertical resolution (mr)** 1.0
Solid angle (msr) 7.8
Transverse length acceptance (cm) ±5
Transverse position resolution (cm) ** 0.1
* (horizontal coordinate on the focal plane)/(target point)
** FWHM

## Slide 5
Impulse Approximation limitations to the (e,e’p) reaction on 208Pb
Identifying correlations and relativistic effects in the nuclear medium
K. Aniol, A. Saha, J.M. Udias, G.M. Urciuoli
Spokepersons
Jlab experiment E06-007
High resolution challenge:

## Slide 6
The goal of the experiment
Use 208Pb, a doubly magic, complex nuclei, a textbook case for the shell model. Measure 208Pb(e,e’p)207Tl cross sections at true quasielastic kinematics and at both sides of q. This has never been done before for A>16 nucleus
Study low lying states in 207Tl :
g.s. 3s1/2
0.351 2d3/2
1.348 1h11/2
1.683 2d5/2
3.470 1g7/2
Quasielastic kinematics: xB = 1, q = 1 GeV/c , ω = 0.433 GeV/c
Determine momentum distributions: 0 < pmiss < 500 MeV/c
Determine ATL by measuring cross sections on either side of q
xB=0.18
Lumjlab/LumNIKHEF-K = 170

## Slide 7
Peak Extraction Procedure
(GEANT Simulation)
Excitation Energy (MeV), pm=100MeV/c
To perform a good peak extraction  1 MeV resolution needed

## Slide 8
Target Issues and choice
Target Issues:
The target have to withstand currents up to 80 uA
The best comprimise between event statistic ( thick target) and resolution ( thin target) had to be found:
Target choice:
Cold Lead in diamond sandwich
A 0.2 mm lead foil sandwiched between two 0.15 mm diamond foils at cryogenic temperatures
Other target used:
Bismuth
Carbon

## Slide 9: Target Orientation

## Slide 10: METHOD TO IMPROVE THE OPTIC DATA BASE: An optical data base means a matrix T that transforms the focal plane coordinates in scattering coordinates:
To change a data base means to find a new matrix T’ that gives a new set of values:
:
Because:
this is perfectly equivalent to find a matrix
you work only with scattering coordinates.
.
From F you simply find T’ by:

## Slide 11: METHOD TO IMPROVE THE OPTIC DATA BASE (II)
Expressing:
You have:
just consider as an example the change in the momentum DP because of the change in the data base:
with
a polynomial expression
Because of the change DPDP’ also the missing energy
will change:
In this way to optimize a data base you have just to find empirically a polynomial
in the scattering coordinates that added to the missing energy improves its resolution
:
and finally to calculate

## Slide 12
An example: Hypernuclear spectroscopy experiment (E94-107)
In the Λ electroproduction on proton (e + p -> e’ + K+ + Λ),
The excitation energy appeared a function of the secondary electron and Kaon scattering variables:
Exictation energy = Constant + P1(DPe, θe, φe, Ye) + P2(DPk, θk, φk, Yk)
With P1(DPe, θe, φe, Ye) + P2(DPe, θe, φe, Ye) are polynomials of the scattered electron and kaon momenta.
A good data base should of course get rid of this unphysical behaviour
It is straightforward to find the correct data base because :
Excitation energy (New data base) = Excitation energy (Old data base) – DM
With DM = - P1(DPe, θe, φe, Ye) - P2(DPk, θk, φk, Yk)
The right data base should produce the changes δ(DPe), δ(θe), δ(φe), δ(Ye), δ(DPk), δ(θk), δ(φk), δ((Yk) for which:
(1)

## Slide 13
Old data base
Improved data base
Elastic
Right arm
Elastic
Left arm
12C(e,e’p)11B
Missing energy
About 1 MeV resolution
Optimization Results