Fiber Bending Light Loss Calculation
4/11/2016
Xiaochao Zheng
R={sqrt( a^2+d^2 )}over{ 4a }
if d>a
%theta={arcsin( {d/2}over{R} )}
fraction of full circle is 2q/(2p)
if d<a
R=d/2
%theta={ %pi }over{ 2 }
fraction of full circle is 0.5

---
from ATLAS Tile Cal TDR (loss with fiber wound a full circle):
Do a linear fit, loss at full circle with radius R(<10cm) is:
5.3% * (10cm – R)
i.e., loss is
40% at R=2.5cm or diameter 5cm;
zero at R=10cm or diameter 10cm.

---
Distance between our fiber holes to center of module: