Status Update of SoLID Ecal Beam Test @FTBF
Jixie Zhang
University of Virginia
March. 11st, 2021

---
Outline
- MWPC cluster finding algorithm
- Ecal gain match
- Preshower gain match
- Merged Ecal and MWPC root files, adding MWPC cluster information
- Started analyzing simulated data
- TODO:
  - Reduce false MWPC clusters and determine beam position cuts
  - Calibration
  - Extract Ecal resolution

---
MWPC Double Peaks
- Double peak exist at each 64-channel-TDC module
- Wire in the first peak is most closed to the incident particle and has the most strong signal

---
MWPC Signals & Time cut
- TDC 1 (wire id from 0 -127)
- Shift by 59
- Time cut is +/-18

---
MWPC Cluster Finding Algorithm
- Step 1) Choose the 1st hit as the seed, search for any hits that are within 2.1 mm distance. Add them into the cluster chain and mark them as used.
- Step 2) Determine the minimum and maximum of the chain. Then use the minimum and maximum as the pivots, search for hits that is within 2.1 mm from the pivot
- Stop searching until Step 2) could not find any more cluster candidates. Now one cluster is found!
- If there are still hits that are not marked as used, use these hits to search for more clusters.
  Note:
- I picked 2.1mm in order to avoid situation that there is one dead wire in between 2 hits. If there are 2 and more continuous dead wires, false cluster will occur.

---
Determine MWPC Cluster Position
- If there are hits in the first peak (where tdc<0), use the tdc value weighted position of the first peak as the cluster position:
  cluster_x = sum (tdc*x) / sum(tdc)
  ignoring all hits in the 2nd peak;
- If there are no hits in the first peak, use the tdc value weighted position of the 2nd peak as the cluster position:
  cluster_x = sum ((19-tdc)*x) / sum(19-tdc)
  Note:
- I linearly weight the position by tdc value, we might also try to do the weighting in the following ways:
  A) cluster_x = sum (tdc^2 * x) / sum(tdc^2)
  B) cluster_x = sum (tdc^0.5 * x) / sum(tdc^0.5)

---
MWPC Cluster: example 0

---
MWPC Cluster: example 1

---
MWPC Cluster: example 2

---
MWPC Cluster: example 3

---
MWPC Cluster: example 4

---
MWPC Cluster: example 5

---
MWPC Cluster: example 6

---
Multiple MWPC Clusters

---
Position Difference Between MWPC
Require only one cluster in both chamber0 and chamber1

---
Cluster Positions
Do not understand this peak!!!

---
Compare Clusters to Hits
No Scaling

---
Compare Clusters to Hits
Scale cluster histogram to match height

---
Gain Match for Ecal, 4 GeV, R=1cm
Fitting the MIP peak
Fitting the e- peak

---
Gain Match for Ecal, 8 GeV, R=1cm
Fitting the MIP peak
Fitting the e- peak

---
Gain Match for Preshower, R=1cm
Fitting the MIP peak, 4 GeV
Fitting the MIP peak, 8GeV

---
Peak Fitting Results
- ch2_main ch3_main ch4_main ch5 ch6 ch7 ch2 ch3 ch4
- double peak4[] = { 7938, 8191, 6990, 127, 56, 141, 675, 759, 617};
- double peak6[] = { 13651, 13803, 11744, 277, 135, 189, 778, 844, 692};
- double peak8[] = { 11860, 12808, 11389, 131, 46, 137, 505, 563, 458};
- double peak10[] = { 15001, 15782, 13856, 130, 57, 132, 485, 542, 436};
- double peak12[] = { 19159, 20728, 18062, 210, 125, 175, 549, 636, 521};
- double peak16[] = { 6884, 7522, 8712, 127, 51, 117, 117, 135, 139};
  Note:
- 1 GeV calibration data do not have MWPC chamber0
- NO 2 GeV calibration data
- Preshower HV almost not changed at all beam energies, except 16 GeV
- 6GeV and 12 GeV has serious pile up issue

---
Signal for 8 Gev Calibration Runs, 1016

---
Signal for 8 Gev Calibration Runs, 1017

---
Signal for 8 Gev Calibration Runs, 1018

---
Pile up … 8 GeV
8 GeV, beam on top block, ~30k particles per spill, 6k triggers per spill

---
Pile up … 10 GeV
10 GeV, beam on top block, ~80k particles per spill, 9k triggers per spill

---
Simulated Result: Ecal only

---
Simulated Result: Ecal and Preshower

---
Summary
- MWPC cluster finding algorithm is developed. But we still need to reduce false cluster and determine a tracking cut
- Merged Ecal and MWPC root files, adding MWPC cluster information
- Ecal gain match is on going
- Preshower gain match is on going
- Started analyzing simulated data
- Building work environment in ifarm, prepare to transfer some tasks to Zhenyu’s group
- TODO:
  - Reduce false MWPC clusters and determine beam position cuts
  - Finish gain matching, then start chi2 fitting to determine matching between preshower and shower
  - Compare to simulation to determine TDC to MeV coefficient
  - Extract Ecal resolution

---
Back up ...

---
Signal Width

---
MWPC Calibration Parameters
Latest MWPC position offsets:
- 174.43 461.83 750.40 1529.55 zz
- 6.332 6.335 6.340 6.347 xi
- 6.370 6.368 6.345 6.358 yi
- 0.45
- 59 58 59 60 50 51 51 52
- 50 50 53 54 50 50 49 48
- 18 | itwin (time window)