SoLID Ecal Calibration
Jixie Zhang
University of Virginia
June 3rd, 2021

---
Outline
- Determine Pedestal
- NEW: removing pileup events
- Integration total ADC
- Merge Ecal and MWPC root files
- Apply gain match of Pre-shower and gain match of shower, extract module ADC weighted cluster position
- TODO:
  - Reduce false MWPC clusters and determine beam position cuts
  - Calibration between pre-shower and Ecal
  - Extract Ecal resolution

---
Methodology
Minimize the width of Etot (defined below) to get 5 parameters using using electron peak of production data:
Etot = (alpha1 * PS1 + Shower1) * 1.0
        + (alpha2 * PS2 + Shower2) * beta2
        + (alpha3 * PS3 + Shower3) * beta3
- Get 0-th order values for alpha1, alpha2, alpha3 using electron peak of calibration data
  - Minimize width of electron (alpha1 * PS1 + Shower1) to get alpha1
  - Minimize width of electron (alpha2 * PS2 + Shower2) to get alpha2
  - Minimize width of electron (alpha3 * PS3 + Shower3) to get alpha3
- Get 0-th order values for beta1 (1.0), beta2, beta3 using pion peak of calibration data
  - Fit Landau-gaus to the MIP peak of each module, then align them to the same location

---
Fitting: if initial parameters are bad ...
6G

---
Fitting: if initial parameters are bad ...
12G

---
Method 1: Check vertical by eyes
1
6G, right block

---
Method 2: Check Width/Mean by Gaussian Fit
1
6G, right block

---
6G Right: Check Peak Value of Each X Slice

---
6G Right: Check Peak Value of Each X Slice

---
6G Right: Check Peak Value of Each X Slice

---
6G Right: Check Peak Value of Each X Slice

---
6G Right: Check Peak Value of Each X Slice

---
6G Right: Check Peak Value of Each X Slice

---
Summary
1) on going, not finish yet

---
Ecal Energy Resolution
6 G after removing pileup: 0.0399
  double dEOverE_old[]={0.061, 0.0405, 0.0489, 0.0386,0.0337, 0.0468};

---
How to Remove Pileup Events?
For each event, search peaks for channel 2-7.
1) remove event if the peak time is out of the range of
(AveragedPeak-5,AveragedPeak+5)
2) remove event if any adc >= 4095 where 15 < time < 40
3) remove event if more than 1 peaks found where 15 < time < 40, requiring the height of the peak not less than 20 and not less than 5% of the maximum peak height
About 765/68357 ~=1.1% events were removed in 6 GeV calibration run 855
About 1051/74211 ~=1.4% events were removed in 12 GeV calibration run 903
About 7941/184141 ~=4.3% events were removed in 16 GeV calibration run 924
About 2772/77621 ~=3.6% events were removed in 4 GeV calibration run 1010
About 2381/97585 ~=2.4% events were removed in 8 GeV calibration run 1013
About 1041/58071 ~=1.8% events were removed in 10 GeV calibration run 1089