Data acquisition for
DVCS experiment
 By Pierre-Henri de La Codre

---
- ARS16vme64
- My work
- Current situation
- Decoding
- Problem
- Schedule

---
ARS16vme64
 •	1 board can acquire 1 event during 128 ns with a sampling frequency of 1 GHz when a trigger is detected.
- Then it transfers the data with very fast VME protocols to the DAQ.
- There are 13 boards and each board has 16 inputs channels .
- We are currently working in MBLT protocol but we will try to make it work in 2esst.

---
My work
Readout ( CODA crl )
Board
Initialization
ARS
CODA
file
Decoding
Display
ROOT
file

---
The current situation
- We are working with the cpu MVME 6100
- We generate a signal and the trigger with a test bench
trigger
signal

---
The test bench
L1A
Trigger
Clock
Test bench
 card
ARS
signal

---
The decoding
- standard bus has two buses of 32 bits each (address and data)
- Each event have 512 data
- They are decode in four parts:
  A: channel 0 to 3
  B: channel 4 to 7
  C:channel 8 to 11
  D: channel 12 to 15

---
We succed in runnig one card sending the previous signal on two entries
Chan 0 -3
Chan 4 -7
Chan 8-11
Chan 12-15
Event counter

---
Problem : acquisition

---
Schedule
- We need to solve the loss of cycle problem and the 0xffffffff problem
- To do that we are currently modifying the decoding software in order to detect the number of failing events and modifying the acquisition to suppress those events