Task Hazard Analysis (THA) Worksheet / (See ES&H Manual Chapter 3210 Appendix T1 / Work Planning, Control, and Authorization Procedure)

Author:	Jack Segal				Date:		08/11/21		Task #: / If applicable
Complete all information. Use as many sheets as necessary
Task Title:		BigBite GRINCH for the SBS experiments			Task Location:			Hall A, downstream of the target and on the beam left side
Division:		Physics			Department:	Hall A		Frequency of use:		Daily from September 2021 onwards
Lead Worker:			Bradley Yale
Mitigation already in place: / Standard Protecting Measures / Work Control Documents				Use of voltage appropriate shielded HV cables and connectors. Restricting orifice and relief valve between regulator and detectors

Sequence of Task Steps	Task Steps/Potential Hazards	Consequence Level	Probability Level	Risk Code (before mitigation)	Proposed Mitigation / (Required for Risk Code >2)	Safety Procedures/ Practices/Controls/Training	Risk Code / (after mitigation
1	Electrical shock from / 2kV high voltage / supplying GRINCH photomultiplier tubes, or / from 6V low voltage power / supply for GRINCH front end / NINO cards	M	L	2	Use of current limited high voltage supply at 2kV. Use of shielded cables and connectors for HV. Use of 4 AWG welding cables and connectors for LV	High voltage cables are only connected or disconnected to/from the detectors, power supplies, and patch panels when power supply is not energized. / ESH Manual Chapter 6200 Electrical Safety Program: / https://www.jlab.org/ehs/ehsmanual/manual/6200.html / / Training: ESC001, ESC003, ESC004, ESC007, and ESC008 Electrical Safety Awareness Class, Modes, etc. / https://www.jlab.org/ehs/ehsmanual/manual/6200.html / Electrical safety training for QEW is currently being modified.	1
2	Use of compressed C4F8 gas: / hazards associated with / handling of pressurized / containers and oxygen / displacement in the event of a / catastrophic leak.	M	L	2	Gas supplied through a / pressure regulator / attached to the gas bottle / with flow limited by a / flow meter, an aperature restriction and a pressure relief valve. / Location of the gas bottle in a / non confined place to limit the / effect of oxygen displacement	Setup, connection, or disconnection of / the gas shall only be done by individuals / authorized by this OSP. / ESH Manual Chapter 6150 Gas Cylinder / Safety - Storage, Movement, and / Labeling / https://www.jlab.org/ehs/ehsmanual/ / manual/6150.html, / Training for individuals: SAF130A, / SAF130C / Relief valve and restriction between the regulator and / detector is implemented as a backup in / the event of regulator failure. / Oxygen deficiency hazard SAF103	1
3	Covid-19 contamination (if at an elevated MEDCON level)	M	M	3	Face covering required. / Maintain Social Distancing of 6’ or use appropriate PPE if 6’ distancing cannot be maintained.	OSP: ESH-21-116798-OSP. / Follow required guidelines	1
4	Use of portable ladder / for access to the GRINCH / detector	M	M	3	Use of ladder training and having an observer/assistant.	SAF307 Ladder Safety	1

Highest Risk Code before Mitigation:	3	Highest Risk Code after Mitigation:	1

When completed, if the analysis indicates that the Risk Code before mitigation for any steps is “medium” or higher (RC≥3), then a formal Work Control Document (WCD) is developed for the task. Attach this completed Task Hazard Analysis Worksheet. Have the package reviewed and approved prior to beginning work. (See ES&H Manual Chapter 3310 Operational Safety Procedure Program.)

Form Revision Summary / Revision 0.2 – 07/26/21 – Periodic Review; updated header and footer / Periodic Review – 08/29/18 – No changes per TPOC / Periodic Review – 08/13/15 – No changes per TPOC / Revision 0.1 – 06/19/12 - Triennial Review. Update to format. / Revision 0.0 – 10/05/09 – Written to document current laboratory operational procedure. / ISSUING AUTHORITY TECHNICAL POINT-OF-CONTACT APPROVAL DATE REVIEW DATE REV. / ES&H Division Harry Fanning 08/29/18 07/26/24 0.2 / This document is controlled as an on line file. It may be printed but the print copy is not a controlled document. It is the user’s responsibility to ensure that the document is the same revision as the current on line file. This copy was printed on 8/13/2021.