fa
	Operational Safety Procedure Form / (See ES&H Manual Chapter 3310 Appendix T1 Operational Safety Procedure (OSP) and Temporary OSP Procedure for instructions.)

Title:	Safe Operation of the Super Big Bite Power Supply and Corrector Magnets' Power Supplies During Commissioning and SBS Experiments
Location:		Hall A					Type:	X OSP / TOSP
Risk Classification / (per Task Hazard Analysis attached) / (See ES&H Manual Chapter 3210 Appendix T3 Risk Code Assignment.)				Highest Risk Code Before Mitigation				3
				Highest Risk Code after / Mitigation (N, 1, or 2):				1
Owning Organization:			Physics		Date:	08/09/21
Document Owner(s):			Jack Segal

DEFINE THE SCOPE OF WORK
Purpose of the Procedure – Describe in detail the reason for the procedure (what is being done and why).
The intent of this procedure is to provide instruction for authorized personnel to safely operate the Super Big Bite Power supply and corrector magnets' power supplies during commissioning and SBS experiments.
Scope – include all operations, people, and/or areas that the procedure will affect.
The operation of the Super Big Bite magnet is anticipated to deflect the beam on the beam dump. To correct this deflection two corrector magnets have been installed on the exit beam line in Hall A. One upstream of the Super Big Bite magnet and one downstream of the Super Big Bite magnet. The required currents in the corrector magnets will need to be established for each desired Super Big Bite magnet current setting and physical position. Each corrector magnet has two coils, each powered by an independent power supply. The Super Big Bite magnet has one power supply driving all its coils in series. The currents of all five power supplies will be monitored by a FSD ADC model Y0512 designed by JLAB.
Description of the Facility – include building, floor plans and layout of the experiment or operation.
One water cooled 2200 amp, 290 volt DC power supply. Four air cooled 330 amp, 10 volt DC power supplies. All five will be remotely controlled using existing software.

ANALYZE THE HAZARDS and IMPLEMENT CONTROLS
Hazards identified on written Task Hazard Analysis
Electrical / Magnetic Field / Fire / Missteering of Beam
Authority and Responsibility:
	Who has authority to implement/terminate
	Yves Roblin, Jay Benesch, Crew Chief
	Who is responsible for key tasks
	Yves Roblin, Jay Benesch
	Who analyzes the special or unusual hazards including elevated work, chemicals, gases, fire or sparks (See ES&H Manual Chapter 3210 Appendix T1 Work Planning, Control, and Authorization Procedure)
	Yves Roblin (accelerator operations) / Jay Benesch (accelerator operations) / Jack Segal (power supplies, electrical) / Jessie Butler (Hall A Work Coordinator)
Personal and Environmental Hazard Controls Including:
	Shielding
	Standard Hall A shielding
	Barriers (magnetic, hearing, elevated or crane work, etc.)
	The entire hall is considered a five Gauss zone.
	Interlocks
	The five power supply faults will be interlocked back to EESSAF to prevent beam steering problems. All five power supplies will be configured such that if one supply trips off it will trip off the other power supplies.
	Monitoring systems
	While the power supplies can be monitored through the EPICS GUIs, remote control of the supplies will only be enabled for MCC.
	Ventilation
	LCW (Low Conductivity Water) / Free Air (fans integral to the power supplies)
	Other (Electrical, ODH, Trip, Ladder) (Attach related Temporary Work Permits or Safety Reviews as appropriate.)
	None
List of Safety Equipment:
	List of Safety Equipment:
	Machine Protection System
	Special Tools:
	The specific procedure for determining the operating parameters for the magnets is being developed by Yves Roblin and Jay Benesch with assistance from David Flay and Bogdan Wojtsekhowski
Associated Administrative Controls
	Standard for beam operations
Training
	What are the Training Requirements (See List of Training Skills)
	Standard training for Accelerator Operators / Authorization from Yves Roblin and Jay Benesch

DEVELOP THE PROCEDURE
Operating Guidelines
Power supplies should be operated within manufacturer’s guidelines and agreed upon limits set for the experiment.
Notification of Affected Personnel (who, how, and when include building manager, safety warden, and area coordinator)
Hall A Run Coordinator. Cell phone: (757) 876-1787 / Crew Chief
List the Steps Required to Execute the Procedure: from start to finish.
Perform pre-job briefing / Verify that permission to operate the power supplies has been given by the Hall A Work Coordinator / Energize power supplies and clear any faults / During commissioning and when beam parameters or the desired SBS magnet settings or physical positions are changed, the allowed beam current will be determined by Accelerator Operations. The parameters for the magnet currents will need to be adjusted by MCC. The SBS and corrector magnets' current FSD's will need to be masked. Yves Roblin, Jay Benesch, or their designee, will raise the currents in the magnets as required to maintain the beam position on the dump. After determining the required magnet currents, the high and low trip points for the magnet currents will be set in the Y0512 FSD ADC. The FSD's for the magnet current will then need to be unmasked. / Incrementally ramp current to power the magnets and check beam position on the dump / Also, verify that the current output from the Super Big Bite and corrector magnets power supplies are stable and uniform between power supplies at the momentum settings for the power supplies
Back Out Procedure(s) i.e. steps necessary to restore the equipment/area to a safe level.
Power down and turn off the power supplies.
Special environmental control requirements:
	List materials, chemicals, gasses that could impact the environment (ensure these are considered when choosing Subject Mater Experts) and explore EMP-04 Project/Activity/Experiment Environmental Review below
	None
	Environmental impacts (See EMP-04 Project/Activity/Experiment Environmental Review)
	None
	Abatement steps (secondary containment or special packaging requirements)
	None
Unusual/Emergency Procedures (e.g., loss of power, spills, injury, fire, etc.)
In the event of injury, or an immediate emergency exists, call 911 and also notify: /  Guards (x5822) /  Occupational Medicine (x7539) /  Crew Chief (x7045) (if inside the fence) / In case of an injury follow standard JLAB procedures. Initial response cards are located with each phone for appropriate emergency phone numbers. Additional information can be found at https://jlabdoc.jlab.org/docushare/dsweb/Get/Document-24400/*.pdf.
Instrument Calibration Requirements (e.g., safety system/device recertification, RF probe calibration)
MPS as required by Accelerator Division
Inspection Schedules
None
References/Associated/Relevant Documentation
Run plan as developed by Yves Robin and Ray Benesch
List of Records Generated (Include Location / Review and Approved procedure)
None

Submit Procedure for Review and Approval (See ES&H Manual Chapter 3310 Appendix T1 OSP & TOSP Instructions – Section 4.2 Submit Draft Procedure for Initial Review):
- Convert this document to .pdf
- Open electronic cover sheet:
https://jlabdoc.jlab.org/docushare/dsweb/Get/Document-24048/3310T1Form.doc
- Complete the form
- Upload the pdf document and associated Task Hazard Analysis (also in .pdf format)

Distribution: Copies to Affected Area, Authors, Division Safety Officer
Expiration: Forward to ES&H Document Control

Form Revision Summary / Revision 1.7 – 02/25/2021 – Corrected link to Word doc; updated ‘ESH&Q’ to “ES&H’; other minor edits. No approval required. / Revision 1.6 – 06/23/2020 – Update section 15 to reflect guard number, what to do in an emergency, crew chief numbers, etc. approved by H. Fanning / Revision 1.5 – 04/11/18 – Training section moved from section 5 Authority and Responsibility to section 9 Training / Revision 1.4 – 06/20/16 – Repositioned “Scope of Work” to clarify processes / Qualifying Periodic Review – 02/19/14 – No substantive changes required / Revision 1.3 – 11/27/13 – Added “Owning Organization” to more accurately reflect laboratory operations. / Revision 1.2 – 09/15/12 – Update form to conform to electronic review. / Revision 1.1 – 04/03/12 – Risk Code 0 switched to N to be consistent with 3210 T3 Risk Code Assignment. / Revision 1.0 – 12/01/11 – Added reasoning for OSP to aid in appropriate review determination. / Revision 0.0 – 10/05/09 – Updated to reflect current laboratory operations / ISSUING AUTHORITY FORM TECHNICAL POINT-OF-CONTACT APPROVAL DATE REVIEW DATE REV. / ES&H Division Harry Fanning 04/11/18 02/25/24 1.6 / This document is controlled as an on line file. It may be printed but the print copy is not a controlled document. It is the user’s responsibility to ensure that the document is the same revision as the current on line file. This copy was printed on 8/15/2021.