## Slide 1
PSU
VC L
H20 DC Bus
H20 DC Bus
VC L
HB Resistance of RT components / VCL at 4K Measured with a HP 3458A meter |  | 
1-A | 0.0014 | Per H20 DC lead
1-B | 0.0018 | One lead and across magnet
2-A | 0.0018 | One lead and across magnet
2-B | 0.0014 | Per H20 DC lead
Vapor Cooled Lead | 0.0004/2 = 0.0002 | Per Lead
C-G | 0.06022 | Dump resistance including flexible cables
E-F | 0.0335 | Resistor bottom
D-E | 0.0305 | Resistor top
C-D F-G | 0.00085 0.00085 | Per Flexible cable pair
1
1
A
2
B
E
C
D
F
Flexible cables
Two in parallel
HB Magnet
4K
RT
G
Flexible cables
Two in parallel